## Slide 1: Analysis and prediction of extreme wind speeds and loads - mysteries and misconceptions
Advances in Wind and Structures AWAS20
August 25-28, 2020
John Holmes
(JDH Consulting, Australia)
Chi-Hsiang Wang
(CSIRO, Australia)

## Slide 2
Analysis and prediction of extreme wind speeds and loads
Extreme value distributions
- Generalized Extreme (GEV) versus Generalized Pareto (GPD)
‘Return period’ versus ‘average recurrence interval’
Separation and correction of recorded wind data
Fitting of GEV /GPD with a fixed shape factor
Topics
‘Bootstrapping’ and confidence limits
Prediction of wind loads and response allowing for wind direction variations
References
Summary and conclusions

## Slide 3
Analysis and prediction of extreme wind speeds and loads
‘Return period’ versus ‘average recurrence interval’
Return period (Gumbel, 1941)
- reciprocal of probability of exceedance of epoch (annual) maximum
Cannot be less than 1,
since a probability cannot be greater than 1
Average recurrence interval
- reciprocal of crossing rate of high values by a stationary random process
Can be less than 1 year
These two quantities are very often conflated!

## Slide 4
Analysis and prediction of extreme wind speeds and loads
‘Return period’ versus ‘average recurrence interval’
Probability of V being the maximum value in time T = probability of zero exceedances in time T
Assume a Poisson Distribution for the number of exceedances, n, of wind speed V in a given time period T:
Mean,
By definition of return period, RP,
Probability of non-exceedance of V in 1 year =
Hence,

## Slide 5
Analysis and prediction of extreme wind speeds and loads
‘Return period’ versus ‘average recurrence interval’
RP > 1

## Slide 6
Analysis and prediction of extreme wind speeds and loads
Separation and correction of recorded wind data
Synoptic (extra-tropical depression):
Separate synoptic wind events from non-synoptic/transient

## Slide 7
Analysis and prediction of extreme wind speeds and loads
Separate synoptic wind events from non-synoptic/transient
Separation and correction of recorded wind data
Non-synoptic (downburst):

## Slide 8
Analysis and prediction of extreme wind speeds and loads
Separation and correction of recorded wind data
Correction for gust duration
~15%

## Slide 9
Analysis and prediction of extreme wind speeds and loads
Separation and correction of recorded wind data
Correction for terrain (by direction sector)
1.6 km
Assess by inspection (e.g. Google Earth images)
Alternatively,
recorded gust factors turbulence intensity  roughness length  correction factor

## Slide 10
Analysis and prediction of extreme wind speeds and loads
Extreme value probability distributions
Generalized extreme value distribution (GEV)
k = shape factor; u = location parameter; a = scale factor
VR = A – B. RI-k
A = u + (a / k); B = (a / k)

## Slide 11
Analysis and prediction of extreme wind speeds and loads
Extreme value probability distributions
Generalized Pareto distribution (GPD)
Average crossing rate of uo = 
VR = A – B. RI-k
A = uo + ( / k);
Distribution for exceedances of a threshold (uo)
Average crossing rate of VR =
GPD

## Slide 12
Analysis and prediction of extreme wind speeds and loads
Extreme value probability distributions (GEV/GPD)
Shape factor (k)
VR = A – B. RI-k
k < 0 VR is unlimited - VR > A for all RI (‘Type 2’ Extreme Value Distribution)
k = 0 VR is unlimited (‘Type 1’ or ‘Gumbel’ Extreme Value Distribution)
VR = u + a logeRI or VR = (+ loge) +  logeRI
k > 0 VR is limited - VR < A for all RI (‘Type 3’ Extreme Value Distribution)
Extreme wind data usually fitted well by a small positive value of k
- the upper limit of A has physical meaning
– e.g. Australian Standards: k = +0.1
Same value of k for GEV and corresponding GPD
(k  0)

## Slide 13
Fitting methods for GPD/GEV with a fixed shape factor, k
Analysis and prediction of extreme wind speeds and loads
VR = A – B. RI-k
Fix k - now only two unknowns: A and B (3 parameter  2 parameter)
Simple fit using ‘peaks over threshold’ data (Method 1)
Set a threshold, uo – e.g. 25 m/s
Calculate average rate of exceedance of uo ,  , e.g. 0.885 per annum
Estimate of /k
e. g. for k = 0.1, /k  11 E
Calculate average of all positive excesses above the threshold, E, e.g. 4.50 m/s
Calculate predicted values for high average recurrence intervals:
This is effectively the ‘Method of Moments’ when k is a fixed value
– only uses the mean excess, standard deviation is not required

## Slide 14
Simple fit using ‘peaks over threshold’ data (Method 1)
Analysis and prediction of extreme wind speeds and loads
 | year | Gust (m/s) | Excess (m/s)
1 | 1991 | 29.2 | 4.2
2 | 1992 | 26.7 | 1.7
3 | 1993 | 26.7 | 1.7
4 | 1994 | 28.2 | 3.2
5 | 1995 | 27.7 | 2.7
6 | 1997 | 32.3 | 7.3
7 | 1997 | 26.2 | 1.2
8 | 1998 | 35.1 | 10.1
9 | 1998 | 31.4 | 6.4
10 | 2003 | 29.8 | 4.8
11 | 2003 | 31.3 | 6.3
12 | 2003 | 26.2 | 1.2
13 | 2005 | 25.9 | 0.9
14 | 2008 | 25.2 | 0.2
15 | 2008 | 27.8 | 2.8
16 | 2010 | 36.8 | 11.8
17 | 2011 | 31.3 | 6.3
18 | 2011 | 28.7 | 3.7
19 | 2012 | 29.7 | 4.7
20 | 2012 | 27.8 | 2.8
21 | 2013 | 27.3 | 2.3
22 | 2014 | 33.8 | 8.8
23 | 2015 | 33.3 | 8.3
 |  | Average E | 4.50
VR = 74.5 – 50.1 RI-0.1
Average rate of exceedance of uo,  = 23/26 = 0.885 per annum
Average excess, E = 4.50 m/s
A = uo + ( / k)
= (49.5)  (0.885)-0.1 = 50.1 m/s
 / k
= 11E = 49.50 m/s
= 25 + 49.50 = 74.5 m/s
Threshold, uo = 25 m/s

## Slide 15
Other fitting methods GPD/GEV with a fixed shape factor, k
Analysis and prediction of extreme wind speeds and loads
Mean exceedance plot (Method 2)
Intercept =
Slope = – k/(1 + k) (known)
Compute mean excess over several thresholds
average of the mean excesses over all N thresholds
(Davison and Smith, 1990)

## Slide 16
Other fitting methods GPD/GEV with a fixed shape factor, k
Analysis and prediction of extreme wind speeds and loads
Direct least-squares fit of GEV to data (Method 3)
Intercept = A
Slope = B
Rewrite VR = A – B. RI-k
y = VR and z = - (RI-k).
intercept

## Slide 17
Other fitting methods GPD/GEV with a fixed shape factor, k
Analysis and prediction of extreme wind speeds and loads
Maximum likelihood (Method 4)
Maximize log likelihood function for GPD:
(Hosking & Wallis, 1987)
Iterative numerical solution is required
‘best’ fit, but cumbersome to use……

## Slide 18
Examples of fits by Methods 1 - 4
Analysis and prediction of extreme wind speeds and loads
Method 1 – simple (MoM)
Method 2 – mean exceedance
Method 3 – direct least squares
Method 4 – maximum likelihood

## Slide 19
‘Bootstrapping’ and confidence limits
Chart: 15 random sample fits
| 20 | 50 | 100 | 200 | 500 | 1000 | 2000 | 5000
 | 34.2461 | 37.3939 | 39.5908 | 41.6405 | 44.1409 | 45.8859 | 47.514 | 49.5002
10 percentile | 35.3862 | 38.9221 | 41.3898 | 43.6923 | 46.501 | 48.4611 | 50.29 | 52.5211
90 percentile | 33.0536 | 35.7954 | 37.7089 | 39.4943 | 41.6722 | 43.1921 | 44.6103 | 46.3403
 | 34.9002 | 38.2708 | 40.623 | 42.8177 | 45.495 | 47.3635 | 49.1068 | 51.2335
 | 33.8332 | 36.8405 | 38.9392 | 40.8974 | 43.2862 | 44.9532 | 46.5087 | 48.4061
 | 34.6004 | 37.8688 | 40.1498 | 42.278 | 44.8743 | 46.6861 | 48.3766 | 50.4389
 | 34.3107 | 37.4806 | 39.6927 | 41.7568 | 44.2747 | 46.0318 | 47.6713 | 49.6714
 | 35.5974 | 39.2053 | 41.7232 | 44.0725 | 46.9384 | 48.9384 | 50.8045 | 53.0809
 | 34.1419 | 37.2542 | 39.4263 | 41.4529 | 43.9251 | 45.6504 | 47.2602 | 49.224
 | 32.5271 | 35.0897 | 36.8781 | 38.5467 | 40.5823 | 42.0028 | 43.3283 | 44.9452
 | 34.9209 | 38.2985 | 40.6557 | 42.855 | 45.5379 | 47.4102 | 49.1572 | 51.2883
 | 33.8676 | 36.8865 | 38.9934 | 40.9592 | 43.3572 | 45.0308 | 46.5923 | 48.4971
random numbers {0:1} converted to wind speed excesses through cumulative distribution function (GPD)
Simulated distributions (original reference for ‘bootstrapping’: Efron, 1979 )
Analysis and prediction of extreme wind speeds and loads

## Slide 20
80% Confidence limits
Chart: 80% confidence limits on V500
| 20 | 50 | 100 | 200 | 500 | 1000 | 2000 | 5000
 | 34.2461 | 37.3939 | 39.5908 | 41.6405 | 44.1409 | 45.8859 | 47.514 | 49.5002
10 percentile | 33.0536 | 35.7954 | 37.7089 | 39.4943 | 41.6722 | 43.1921 | 44.6103 | 46.3403
90 percentile | 35.6596 | 39.2887 | 41.8214 | 44.1844 | 47.0671 | 49.0789 | 50.9559 | 53.2457
Analysis and prediction of extreme wind speeds and loads
‘Bootstrapping’ and confidence limits
- based on 144 station-years of daily gust data

## Slide 21
Methods of treating directionality
Analysis and prediction of extreme wind speeds and loads
For prediction of wind loads or structural response
Multi-sector method (Holmes, 1990). Probability distributions fitted to wind speeds for each direction sector. Combined with directional response coefficients to give probability distributions of response per sector.
Combined probability calculated by:
1 – P(> M) = {1 – P(> Mdir1)} {1 – P(> Mdir2)} …… {1 – P(> MdirN)}
Accurate …. only assumption, statistical independence of wind speeds from adjacent direction sectors. Works best with long wind data records
Can be applied to wind speeds (Vdir,i) or to loads such as base moments (Mdir.i)

## Slide 22
Multi-sector method
In terms of return periods, (RP):
=
In terms of average recurrence intervals, (RI):
=
since,
Analysis and prediction of extreme wind speeds and loads

## Slide 23
Out-crossing method (Davenport, 1977; Lepage-Irwin, 1985):
is difficult to calculate accurately from intermittently sampled wind data
many mathematical assumptions in the derivation
assumes that extreme wind events are from the general population of winds
parent distribution (e.g. Weibull)
UR
wind tunnel
climate analysis
Analysis and prediction of extreme wind speeds and loads
applicable to: “….’well-behaved’ wind climates principally associated with large-scale
pressure systems..” Davenport (1977)
U is a mean wind speed from the entire population;  is wind direction

## Slide 24
IHFBB benchmark Building B
Fitted to averaged w.t. data from 7 groups
(every 10 degrees)
180 m
30 m
45 m
y
x
z

defines ‘response boundary’ in outcrossing method
Analysis and prediction of extreme wind speeds and loads
Peak base moments measured by seven wind-tunnel groups
(Holmes & Tse, AWAS/ACEM 2012)

## Slide 25
Generic building assumed to be located near Melbourne Airport
N
8 different orientations with respect to the Melbourne Airport wind climate
Analysis and prediction of extreme wind speeds and loads

## Slide 26
Generic building assumed to be located near Melbourne Airport
N
8 different orientations with respect to the Melbourne Airport wind climate
Analysis and prediction of extreme wind speeds and loads
0 degrees
90 degrees

## Slide 27
Predictions of extreme base moments
0 degrees
+Y
+Z
+X
Outcrossing - good agreement
(N wind is dominant - alongwind for Mx; crosswind for My)
Multisector slightly conservative at low ARIs
Analysis and prediction of extreme wind speeds and loads

## Slide 28
Predictions of extreme base moments
90 degrees
+Y
+Z
+X
Out-crossing poor for My
(W is dominant wind direction – crosswind poorly predicted)
Multisector slightly conservative for Mx
Analysis and prediction of extreme wind speeds and loads

## Slide 29
Summary and Conclusions
Predictions of wind loads and response require consideration of wind direction
‘Multi-sector’ - good agreement with direct calculation of base moments on generic building
‘Out-crossing’ – underpredicts responses in some cases; not suitable for mixed wind climates
GEV and GPD are equivalent – fitting methods may vary.
Ideally confidence limits should be determined. ‘Bootstrapping’ is a good way.
Four different ways of fitting GEV/GPD with a fixed shape factor
‘Return period’ and ‘average recurrence interval’ are different concepts
Extreme winds from different storm types should be separated before extreme value distributions are fitted
Correct for terrain variations & gust duration if instruments change
Notes: 29

## Slide 30
References
E.J. Gumbel (1958). Statistics of Extremes, Columbia University Press, (Dover reprint 2004).
C-H. Wang and J.D. Holmes (2020). Exceedance rate, exceedance probability and the duality of GEV and GPD for extreme hazard analysis, Natural Hazards, Vol. 102, pp 1305-1321.
J.R.M. Hosking and J.R. Wallis (1987). Parameter and quantile estimation for the Generalized Pareto Distribution, Technometrics, Vol. 29, pp 339-349.
A.C. Davison and R.J. Smith (1990). Models for exceedances over high thresholds, Journal of the Royal Statistical Society, Series B, Vol. 52, pp 393-442.
Extreme value distributions and fitting methods
A. Naess and P.H. Clausen (2001). Combination of the peaks-over threshold and bootstrapping methods for extreme value prediction, Structural Safety, Vol. 23, pp 315-330.
P.dZ. Bermudez and S. Kotz (2010). Parameter estimation of the generalized Pareto distribution - Part 1, Journal of Statistical Planning & Inference, Vol. 140, pp 1353-1373.
E.J. Gumbel (1941). The return period of flood flows, Annals of Mathematical Statistics, Vol. 12, pp 163-190.
B. Efron (1979). Bootstrap methods: another look at the jacknife, Annals of Statistics, Vol. 7, pp 1-26.
Notes: 30

## Slide 31
References
A.G. Davenport, (1977). The prediction of risk under wind loading. 2nd International Conference on Structural Safety and Reliability, Munich, Germany, September 19-21.
M.F. Lepage and P.A. Irwin (1985). A technique for combining historical wind data with wind tunnel tests to predict extreme wind loads. 5th U.S. National Conference on Wind Engineering, Lubbock, Texas, November 6-8.
J.D. Holmes (1990). Directional effects on extreme wind loads. Civil Engineering Transactions, Institution of Engineers, Australia, Vol. 32, pp 45-50.
J.D. Holmes (2020). Comparison of probabilistic methods for the effects of wind direction on structural response, Structural Safety, Vol. 87, November 2020, 101983
Prediction of structural loads and directionality
Notes: 31

## Slide 32
References
J.D. Holmes and T.K.T. Tse (2012). International high-frequency base balance benchmark study. 2012 World Congress on Advances in Civil, Environmental and Materials Research (ACEM12), Seoul, Korea, 26-29 August 2012.
S.A. Bekele and J.D. Holmes (2014). Effects of directionality on wind load and response predictions. 2014 World Congress on Advances in Civil, Environmental and Materials Research (ACEM14), Busan, Korea, 24-28 August 2014.
AWAS / ACEM
Notes: 32

## Slide 33: john.holmes@jdhconsult.com